## Slide 1: Senior Design Project I
Week 8: Finalizing Project Idea
Presenter: Josheb P. Dayrit
Notes: For today’s presentation, I have 4 objectives.
To talk about design requirements
To talk about design constraints
To talk about the materials necessary for the project
To talk about my timeline
I’ve also decided to name my project “Sign AI,” so if you see it on the PowerPoint, it’s basically just a term I’m using to refer to my project.

## Slide 2: Background & Motivation
The “What” and “Why”
The “What” - An AI-based ASL translation tool hosted on the Raspberry Pi.
- Uses sEMG (surface electromyography) methods for gesture classification.
- Translates word-by-word.
The “Why” - To enable better communication between the deaf and non-deaf.
Notes: So here’s a list of materials that I’m going to require for my project. Now a lot of them are self-explanatory, but I should probably explain a few.
The Raspberry Pi is linux-based, so I’m going to need an emulator for it on my Windows computer.
Also, the Raspberry Pi has no pins for analog inputs! But there’s various accessories that you can use to sidestep that problem.

## Slide 3: Objectives
The User Perspective
Qualities to aim for:
  Easy-to-use, does not require a lot of manual configuration.
  Portable, can be brought anywhere without undue hassle.
  Non-invasive (surface EMG vs intramuscular EMG).
Notes: So here’s a list of materials that I’m going to require for my project. Now a lot of them are self-explanatory, but I should probably explain a few.
The Raspberry Pi is linux-based, so I’m going to need an emulator for it on my Windows computer.
Also, the Raspberry Pi has no pins for analog inputs! But there’s various accessories that you can use to sidestep that problem.

## Slide 4: Design Requirements
The Must-Haves
The translation tool hosted on a Raspberry Pi must be able to classify gestures through their produced waveforms with, at least, 90% accuracy. Naturally, while higher accuracy percentages are desired, 90% will be the project’s target.
A text-to-speech function via eSpeak will be implemented to convert the classified gesture to spoken word.
On a website run by Dr. Bill Vicars, an ASL professor and deaf person himself, there is a list of 100 words which are commonly-used in everyday ASL conversations. Sign AI will be translating these specific words.
Notes: As far as design requirements go, there are quite a few.
1st design requirement would be the accuracy benchmark. For the machine learning model, the accuracy benchmark that I’m aiming for is 90%. I’ve seen other ASL-related projects reach an accuracy of 90%, so I’m assuming that’s also possible for my project.
The second: a TTS function will also be necessary to speak out the gestures. It’ll be taking inputs from the machine learning model.
Speaking of those inputs, I’m limiting the translation capability of my model to 100 words. An ASL professor compiled a list of commonly-used words in sign language, and it just so happens that the list is composed of 100 words.

## Slide 5: Design Constraints
Limitations
Or, to be more specific, limitation (singular) – there’s just one.
In ASL, some words are expressed through the face, not through the hands. With the current setup, these words cannot be measured by the MyoWare Muscle Sensor.
Notes: So, let’s move on to design constraints. Number 3 is self-explanatory, so I’ll shed some light on number 1 and 2.
1. For limitation number 1, it’s all about language complexity. In any language – English, or whatever your native tongue is, there are multiple ways of expressing a singular idea. And obviously, in my project, I can’t possibly cover all bases. So I’m only going to be translating SVO sentences.
2. Also, some ASL gestures aren’t actually gestures. Sometimes you can convey meaning by pointing, looking at someone, or making faces. I can’t reliably capture those gesture with my chosen sensor. So they’re outside the scope of my project.

## Slide 6: Tasks
Parallel is the keyword
Weeks 1-22: Data Collection and Processing
Data will be in the form of digitized waveforms collected by the MyoWare sensor.
Additionally,
Per person, the waveforms produced by three different muscle groups will be observed.
Data will be truncated to exclude unnecessary parts (i.e. periods of idleness where nothing is being signed).
All test subjects will have diversified heights and builds to account for any effects that physiology might have on data.
Notes: So, let’s move on to design constraints. Number 3 is self-explanatory, so I’ll shed some light on number 1 and 2.
1. For limitation number 1, it’s all about language complexity. In any language – English, or whatever your native tongue is, there are multiple ways of expressing a singular idea. And obviously, in my project, I can’t possibly cover all bases. So I’m only going to be translating SVO sentences.
2. Also, some ASL gestures aren’t actually gestures. Sometimes you can convey meaning by pointing, looking at someone, or making faces. I can’t reliably capture those gesture with my chosen sensor. So they’re outside the scope of my project.

## Slide 7: Tasks
Parallel is the keyword
Weeks 1-22: Prepping Data for AI in an Excel File
Statistical information is going to be extracted from the digitized waveforms and packaged in an Excel file, which will be used as training data for the AI.
Examples of the kind of information that will be extracted:
  Mean time before transitions (1 to 0, 0 to 1)
  Total time in states (how long was the digitized waveform at 0 or 1?)
  Mean time in states (average time at 0 or 1)
  Number of state changes (to 0 or 1)
Notes: So, let’s move on to design constraints. Number 3 is self-explanatory, so I’ll shed some light on number 1 and 2.
1. For limitation number 1, it’s all about language complexity. In any language – English, or whatever your native tongue is, there are multiple ways of expressing a singular idea. And obviously, in my project, I can’t possibly cover all bases. So I’m only going to be translating SVO sentences.
2. Also, some ASL gestures aren’t actually gestures. Sometimes you can convey meaning by pointing, looking at someone, or making faces. I can’t reliably capture those gesture with my chosen sensor. So they’re outside the scope of my project.

## Slide 8: Tasks
Parallel is the keyword
Weeks 1-22: Training AI on TensorFlow
Self-explanatory. The wait will be long. And it will be worth it.
Notes: So, let’s move on to design constraints. Number 3 is self-explanatory, so I’ll shed some light on number 1 and 2.
1. For limitation number 1, it’s all about language complexity. In any language – English, or whatever your native tongue is, there are multiple ways of expressing a singular idea. And obviously, in my project, I can’t possibly cover all bases. So I’m only going to be translating SVO sentences.
2. Also, some ASL gestures aren’t actually gestures. Sometimes you can convey meaning by pointing, looking at someone, or making faces. I can’t reliably capture those gesture with my chosen sensor. So they’re outside the scope of my project.

## Slide 9: Tasks
Parallel is the keyword
Weeks 1-22: Refining AI
We’re refining for accuracy. This can come in the form of collecting more data or extracting more information from waveforms.
Notes: So, let’s move on to design constraints. Number 3 is self-explanatory, so I’ll shed some light on number 1 and 2.
1. For limitation number 1, it’s all about language complexity. In any language – English, or whatever your native tongue is, there are multiple ways of expressing a singular idea. And obviously, in my project, I can’t possibly cover all bases. So I’m only going to be translating SVO sentences.
2. Also, some ASL gestures aren’t actually gestures. Sometimes you can convey meaning by pointing, looking at someone, or making faces. I can’t reliably capture those gesture with my chosen sensor. So they’re outside the scope of my project.

## Slide 10
Today
Aug
Sep
Oct
Nov
Dec
2020
Feb
Mar
Apr
May
Aug 25 - Oct 25
Idea Conceptualization
Collection of Materials
Oct 15 - Oct 25
Raspberry Pi Setup
Oct 25
Oct 25 - Jan 25
Data Collection
Oct 25 - Jan 25
Feature Extraction
Training of AI
Oct 25 - Jan 25
Troubleshooting
Oct 25 - May 5
Jan 25 - May 5
Model Refinement
Timeline
Notes: So, here’s a rough timeline for all my activities. The ones highlighted in red are the most important ones.
The timeline is still tentative, so things can still change.