## Slide 1: Senior Design Project I
Week 9: Design of Sign AI, an AI-Based ASL Translation Tool
Presenter: Josheb P. Dayrit
Notes: For today’s presentation, I have 4 objectives.
To talk about design requirements
To talk about design constraints
To talk about the materials necessary for the project
To talk about my timeline
I’ve also decided to name my project “Sign AI,” so if you see it on the PowerPoint, it’s basically just a term I’m using to refer to my project.

## Slide 2: Background & Motivation
Difficult to find work
National Deaf Center on Post-Secondary Outcomes reveal an alarming truth about deafness: “In 2014, only 48% of deaf people were employed.”
In an American study which closely scrutinized successful discrimination lawsuits made against companies, the EEOC (Equal Employment Opportunity Commission) concluded that “young people who are deaf or hard of hearing should anticipate some resistance from employers.”
Disparities in opportunities and (to some extent) outcomes are due in large part to physical disabilities.

## Slide 3: Background & Motivation
Barriers to employment
Deaf people face many barriers of entry regarding employment, but communication is, by far, the most pressing issue.
In the workplace, collaboration among employees is important. Typically, company projects are completed not by a single person, but by teams of people making collective contributions. A pre-requisite to effective collaboration is effective communication.
Deaf persons have a hard time expressing their ideas to non-deaf persons, because sign language is fundamentally different to spoken language.

## Slide 4: Objective
The gist
The objective of Sign AI is to, quite literally, give a voice to deaf persons.
The inability to speak properly is one disadvantage of deaf persons that either prevents them from fully pursuing specific career paths or leads them to be unjustifiably discriminated against in their search for employment.
This inability stems from the fact that speech is a product of both the ears and the mouth.
Notes: So here’s a list of materials that I’m going to require for my project. Now a lot of them are self-explanatory, but I should probably explain a few.
The Raspberry Pi is linux-based, so I’m going to need an emulator for it on my Windows computer.
Also, the Raspberry Pi has no pins for analog inputs! But there’s various accessories that you can use to sidestep that problem.

## Slide 5: Design Requirements
The Must-Haves
One AI must be able to classify gesture with, at least, 90 percent accuracy. Naturally, while higher accuracy percentages are desired, 90 percent will be the project’s target. Similar projects have achieved this, which means it is possible.
Another AI must be able to unscramble the translated gestures into proper sentences. Sentence structure in ASL is different from sentence structure in standard English. Similar language-based AI (like GPT-2) have been able to accuracy values ranging from 70 to 90 percent. This accuracy range will be the project’s target for this AI.
A text-to-speech function will be implemented to convert the classified gesture to spoken word.
On a website run by Dr. Bill Vicars, an ASL professor and deaf person himself, there is a list of 100 words which are commonly-used in everyday ASL conversations. Sign AI will be translating these specific words.

## Slide 6: Design Constraints
Limitations
Or, to be more specific, limitation (singular) – there’s just one.
In ASL, some words are expressed through the facial expressions, not through the hands. With the current setup, these words cannot be measured by the MyoWare Muscle Sensor.

## Slide 7: Design Approach
A step-by-step breakdown
First, data is collected by the EMG sensors. Data will be in the form of raw EMG waveforms. Four sensors in total will be used for data collection. They will be placed close to the major muscle groups in the arm (biceps and triceps) and shoulder (deltoids), as well as the wrist. When gestures are made, these parts of the body are involved most.
Second, this data will be formatted for training on the AI. This can be done in many ways. The goal is to be able to capture key information about the recorded EMG waveforms.
Finally, the AI will be trained on the formatted data.
Real-time testing comes afterwards, and if accuracy values are not at the target level, the AI will be refined. Some ways to do this would be to collect more data or re-format pre-existing data to better express the waveforms to the AI.

## Slide 8: Design Approach
Another AI?
Another AI will be developed in parallel. While the other AI is for gesture classification, this AI is for unscrambling the translated gestures into sentences. The way you form sentences in ASL is different from standard English, which necessitates this “unscrambling” process.
This AI will be trained the same as the previous AI.
In addition, it will also take inputs from the previous AI.

## Slide 9: System Description
An overview
The AIs are going to be hosted on a Raspberry Pi 3 Model B.
TensorFlow through Python will be used to train both AIs.
The MyoWare Muscle Sensor will be used for data collection. There are 4.
Since the Pi is not able to accept analog inputs, an analog-to-digital converter will be required alongside the EMG sensors.
The Adafruit I2S 3W Stereo Speaker Bonnet alongside a speech synthesizer (eSpeak) will be used to vocalized outputs.

## Slide 10: System Diagram
Deep Neural Networks
TTS
ADC Converter
Raspberry Pi
TensorFlow
Formatted Datasets
Deep Neural Networks
Adafruit Speaker Bonnet
eSpeak
TTS